KAT IIC Controller Register Map

Name	Offset	Length	Function
OPFIFO	0x2	0x2	Setting Bit 10 will terminate the IIC byte access with a STOP Sequence and send a “No Acknowledge” with on the associated read. / Setting Bit 9 will initiate the IIC byte access with a START Sequence. / When bit 8 is high the byte transfer is a read, when low a write. / Bits 7:0 contain the data to be written and are unused in the write case / This FIFO will latch on a LSByte write.
RXFIFO	0x6	0x2	Bits 7:0 of this FIFO contains the data read during a byte read transfer. / This FIFO will latch on a LSByte read.
STATUS	0x8	0x4	Bit[0] RXFIFO empty flag / Bit[1] RXFIFO full flag / Bit[2] RXFIFO overflow error latch / Bit[4] OPFIFO empty flag / Bit[5] OPFIFO full flag / Bit[6] OPFIFO overflow error latch / Bit[8] NACK on write error latch / Any write to these register will clear all latches and reset all fifos
CTRL	0xc	0x4	Setting Bit[0] will lock the op fifo, allowing multiple operations to be queued. This is useful in high latency environment where IIC devices are likely to timeout. Clearing bit[0] fill unlock the fifo, allowing operations to commence.

KAT IIC Notes

OPFIFO and RXFIFO are 32 deep.

KAT ADC / KAT IIC Examples (From UBoot)

Note: when entering Uboot commands ensure operations are entered all at once otherwise iic device will timeout

To Access Local (Ambient) Temperature on TMP421 (IIC ADDR 0x4C, REGISTER ADDR 0x0)

mw d0040000 298; # START, WRITE, DATA=0x98 (4C << 1 + 0x0(IIC WRITE))
mw d0040000 000; # WRITE, DATA=0x00 (Register Address)
mw d0040000 299; # START(REPEATED), WRITE, DATA=0x99 (4C << 1 + 0x1(IIC READ))
mw d0040000 500; # STOP, READ
md d0040004 1; # Read Data from RXFIFO

mw d0040000 298; mw d0040000 000; mw d0040000 299; mw d0040000 500; md d0040004 1;

To Access ADC Temperature on TMP421 (IIC ADDR 0x4C, REGISTER ADDR 0x1)

mw d0040000 298; # START, WRITE, DATA=0x98 (4C << 1 + 0x0(IIC WRITE))
mw d0040000 001; # WRITE, DATA=0x01 (Register Address)
mw d0040000 299; # START(REPEATED), WRITE, DATA=0x99 (4C << 1 + 0x1(IIC READ))
mw d0040000 500; # STOP, READ
md d0040004 1; # Read Data from RXFIFO

mw d0040000 298; mw d0040000 001; mw d0040000 299; mw d0040000 500; md d0040004 1;

To Write EEPROM DATA (IIC ADDR 0x51, ADDR 0x4, DATA 0xDEADBEEF)

mw d0040000 2A2; # START, WRITE, DATA=0xA2 (0x51 << 1 + 0x0(IIC WRITE))
mw d0040000 004; # WRITE, DATA=0x04 (Register Address)
mw d0040000 0de; # WRITE, DATA=0xde
mw d0040000 0ad; # WRITE, DATA=0xad
mw d0040000 0be; # WRITE, DATA=0xbe
mw d0040000 4ef; # WRITE, DATA=0xef

mw d0040000 2A2; mw d0040000 004; mw d0040000 0de; mw d0040000 0ad; mw d0040000 0be; mw d0040000 4ef;

To READ EEPROM DATA (IIC ADDR 0x51, ADDR 0x4)

mw d0040000 2A2; # START, WRITE, DATA=0xA2 (0x51 << 1 + 0x0(IIC WRITE))
mw d0040000 004; # WRITE, DATA=0x04 (Register Address)
mw d0040000 2A3; # START(REP), WRITE, DATA=0xA2 (0x51 << 1 + 0x1(IIC READ))
mw d0040000 100; # READ
mw d0040000 100; # READ
mw d0040000 100; # READ
mw d0040000 500; # STOP, READ
md d0040004 1;
md d0040004 1;
md d0040004 1;
md d0040004 1;

To SET ADC1 PCA9555 Output 0 [7:0] to enabled (IIC ADDR 0x21, ADDR 0x6)

mw d0040000 242; # START, WRITE, DATA=0x42 (21 << 1 + 0x0(IIC WRITE))
mw d0040000 006; # WRITE, DATA=0x06 (Register Address)
mw d0040000 400; # STOP, WRITE, DATA=0x00 (OE_n [7:0] = 0x0)

To SET ADC1 PCA9555 Output 0 [7:0] (IIC ADDR 0x21, ADDR 0x2, Data 0xF0)

mw d0040000 242; # START, WRITE, DATA=0x42 (21 << 1 + 0x0(IIC WRITE))
mw d0040000 002; # WRITE, DATA=0x02 (Register Address)
mw d0040000 4F0; # STOP, WRITE, DATA=0xF0